SECTION 122113

HORIZONTAL LOUVER BLINDS

PART 1	GENERAL

1.1	SUMMARY

A.	Section Includes:

1.	Horizontal slat louver blinds.

2.	Operating hardware.

B.	Related Sections:

1.	Section 061000 - Rough Carpentry: Blocking for support of window blind assemblies.

2.	Section 092100 - Plaster and Gypsum Board Assemblies: Gypsum board substrate for window shade systems.

3.	Section 260000 - Electrical: Connections to electrical motor control system and lighting control system components.

4.	Section 260936 – Modular Dimming Controls: GRAFIK Eye QS control system for roller shades.

5.	Section 274100 – Audio-Video Systems: Connections to audio/visual equipment.

1.2	REFERENCES

A.	National Fire Protection Association (NFPA) 70 - National Electrical Code.

1.3	SUBMITTALS

A.	Submittals for Review:

1.	Shop Drawings: Indicate blind locations, opening sizes, window depth, mounting type, return depth, locations of window operating hardware, power supply locations, and wiring diagrams.

2.	Product Data: Describe blind construction and finishes for slats, headrails, and accessories.

3.	Samples: 8 inch long slat samples of each specified color

B.	Closeout Submittals:

1.	Operation and Maintenance Data: Provide wiring diagrams, system control description, operational requirements, and reprogramming information.

1.4	QUALITY ASSURANCE

A.	Manufacturer Qualifications:

1.	Minimum 5 years of experience in manufacture of low-voltage motorized systems.

2.	Provide single source for blinds and control systems.

B.	Installer Qualifications: Qualified by factory training and previous experience to install and commission specified products.

C.	Perform work in accordance with NFPA 70.

D.	Mockup:

1.	Provide mockup of one typical blind.

2.	Include blind, electrical connections, and controls.

3.	Locate where directed.

4.	Demonstrate operation throughout all cycles.

5.	Approved mockup may remain as part of the Work.

1.5	PROJECT CONDITIONS

A.	Do not install blinds until painting and finishing work is complete.

1.6	WARRANTIES

A.	Furnish manufacturer’s warranty providing coverage for repair or replacement of defective components up to following amounts:

1.	Up to 5 years after date of Substantial Completion: 100 percent of cost of replacement parts.

2.	5 to 8 years after date of Substantial Completion: 50 percent of cost of replacement parts.

1.7	MAINTENANCE

A.	Manufacturer:

1.	Provide 24-hour, 7-day technical support for troubleshooting and programming.

2.	Make replacement parts available for minimum of 10 years after date of manufacture.

PART 2	PRODUCTS

2.1	MANUFACTURERS

A.	Contract Documents are based on Lutron Venetian Blind with Intelligent Tilt Alignment by Lutron Electronics Co., Inc.; 7200 Suter Road, Coopersburg, PA 18036-1299 Telephone (800) 523-9466

B.	Substitutions: Under provisions of Section 013300.

2.2	COMPONENTS - BLINDS

A.	Louver Slats: 2 inches wide, prefinished 0.008 inch thick aluminum horizontal slats with radiused corners.

**** OR ****

B.	Louver Slats:

1.	2 inches wide, solid wood horizontal slats, rectangular with square corners, ends finished to match slat finish.

2.	Wood Species: Cherry, Mahogany, Oak, Pine or Natural Hardwood.

3.	Apply fire-retardant treatment.

C.	Slat Support: Woven thin ladders or Wide decorative tapes.

D.	Head Rail:

1.	2.25 inches deep x 3.75 inches tall.

2.	Prefinished extruded aluminum channel, internally fitted for hardware required for motorized blind operation.

E.	Bottom Rail: Prefinished rolled steel with color-coordinated end caps or Solid wood with species to match louver slats.

F.	Cord: Color coordinated to slat material and finish.

G.	Support Brackets: Suitable for wall, ceiling, or jamb mounting, formed steel, shaped to match head rail, allowing removal of head rail without removing bracket.

H.	Valance: Material to match louver slats with returns to match headrail depth.

2.3	COMPONENTS - DRIVE UNITS

A.	System Description:

1.	Ultra-quiet, precision-controlled electronic drive unit housed inside head rail, independently controlling blind lift and tilt.

2.	Audible noise: Maximum 44 dBA measured 3 feet from electronic drive unit.

3.	Allow for maximum of 100 device interfaces including blinds, keypads, lighting controls, and power supplies.

4.	Allow for 100 zones including blinds and lighting zones.

B.	Power Requirements:

1.	24 VDC input provided by approved NEC Class 2 power source.

2.	One power supply output per electronic drive unit.

3.	Each electronic drive unit powers one blind.

C.	System Performance:

1.	One-touch control of blinds by means of keypad, lighting control, infrared remote, or RF remote.

2.	Capable of stopping bottom rail within accuracy of 0.125 inch at any point between open and close limits.

3.	Capable of rotating slats to minimum of 60 tilt positions.

4.	Capable of aligning tilt to within 1/16 inch of adjacent blinds.

5.	Store preset lift and tilt positions at any stop point along travel along with full open and full close limits for lift and tilt.

6.	Presets set by 5-second button push and hold from keypad, or lighting control.

7.	Move bottom rail of adjacent blinds with different electronic drive units in unison and alignment within 0.125 inch.

8.	Open and close limits programmable from electronic drive unit, keypad, lighting control, or handheld remote control for lift.

9.	Power failure memory.

10.	System components electro static discharge protected.

11.	Tilt control capable of electronic adjustment to limit tilt range for specific applications.

D.	Grouping:

1.	Keypads can control any electronic drive unit, group, or subgroup, or additional interface.

2.	System groups and subgroups configured at point of control without rewiring and without access to electronic drive unit.

3.	System may contain multiple electronic drive units.

4.	Controls able to operate any group or subgroup of electronic drive units regardless of window treatment type.

E.	Integration:

1.	Electronic drive units integrate with lighting controls without separate interface.

2.	Contact closure, R232, and Ethernet interfaces available to interface with audio/visual equipment and security systems.

F.	System Controls:

1.	Blinds controlled by built-in blind columns on lighting control or by keypad.

2.	Electronic drive units, keypads, and lighting controls contain microprocessors, allowing high level programming from any source.

3.	Blinds, lighting controls, and keypads wired together on same communications link.

G.	Open Loop Solar Adaptive Algorithm:

1.	Design system to:

a.	Optimize daylight.

b.	Provide manual override capability for occupants via wall mounted keypad or simple remote control.

c.	Maximize occupants connectivity with outdoors by optimizing view.

d.	Provide diffuse daylight and minimize direct sunlight in the space to reduce solar heat gain and maximize occupants’ comfort in space.

e.	Reduce glare.

f.	Start, stop, and track blinds along same facade in unison for both lift and tilt.

g.	Independently control and adjust lift and tilt.

2.	Hardware: Independent operation of solar tracking program through non-Windows based operating system provided in one or more light management panels.

3.	Control software:

a.	Calculates sun’s position in sky relative to building, then calculates when blind movement is necessary, by facade.

b.	Calculates position of blind to limit direct sunlight penetration to predetermined limit.

4.	Use following inputs for start up:

a.	Building location.

b.	Facade orientation.

c.	Window dimensions.

d.	Solar depth of penetration

e.	Number of blind movements per day.

5.	Do not require user to make daily changes to programming or overall system functionality unless desired.

6.	User interface:

a.	PC graphic user interface: Provide access to adjustable parameters of solar depth of penetration and number of blind movements per day.

b.	Manual override:

1)	Temporary override of control program available through optional manual keypads.

2)	Keypads capable of providing manual control of blinds in particular area, with independent control for lift and tilt.

2.4	CONTROLS AND ACCESSORIES

A.	Wall Mounted Controls:

1.	Low voltage keypads:

a.	Electronically set and reconfigure blind open and close limits for lift, blind preset positions for lift, system groups, and system subgroups without rewiring or access to electronic drive unit.

b.	Fit into standard electrical box.

2.	Face plates:

a.	Attach without visible means of attachment.

b.	Engraved artwork.

3.	Product color: Match NEMA WD1.

4.	Provide immediate local LED response upon button activation.

5.	Backlit buttons.

6.	Removable button assemblies allowing field changes.

7.	Capable of simultaneously controlling one or more blinds.

8.	Type: Two button, Three button, Three button with tilt, Four button with tilt and infrared reception, Four button for dual mount or two group applications, Six button for dual mount or two group applications, Five button with tilt or Multi-group keypad for control of multiple groups of blinds.

B.	Infrared Receivers:

1.	Available on system keypads, as attachment to electronic drive unit, or on system contact closure input board.

2.	Electronically set and reconfigure blind open and close lift limits, blind lift preset points, system groups, and system subgroups without rewiring and without access to electronic drive unit.

3.	Include circuitry to reduce degraded performance.

4.	Type: Open/close handheld transmitter, Open/preset/close handheld transmitter, Three preset handheld transmitter, Multi-function handheld transmitter or Dual group open/preset/close handheld transmitter.

C.	Handheld Remotes: Lutron Sivoia QS Hand-Held Infrared Transmitter.

**** OR ****

D.	Handheld Remotes: Lutron Hand-Held RF Transmitter.

E.	Infrared Interfaces:

1.	Interface to other control system via dry contact closure input device.

2.	Interface with Lutron GRAFIK Eye System.

F.	Transformers:

1.	Electronic drive units powered with 24 VDC power supply; power supplied via NEC Class 2 power source.

2.	Provide individual power supply for each electronic drive unit or power panel including 10 individual power supplies.

2.5	FABRICATION

A.	Fabricate blinds to fit openings with uniform edge clearance of 1/4 inch.

B.	At openings requiring multiple blind units, provide separate blind assemblies with space of 1/2 inch between assemblies, occurring at window mullion centers.

2.6	FINISHES

A.	Louver Slats: Manufacturer’s standard brushed finish or baked enamel.

**** OR ****

B.	Louver Slats: Manufacturer’s standard stained finish or painted finish.

**** OR ****

C.	Louver Slats: Manufacturer’s standard clear finish or Custom finish to match Customer-supplied sample.

D.	Head Rails and Brackets: Color coordinated to louver slats.

E.	Bottom Rail: Finish to match slats.

F.	Ladders and Cords: Color coordinated to louver slats.

G.	Tapes: Color to be selected from manufacturer's standards.

H.	Valance: Finish to match louver slats.

PART 3	EXECUTION

3.1	INSTALLATION

A.	Install blinds in accordance with manufacturer's instructions.

B.	Secure with concealed fasteners.

C.	Installation Tolerances:

1.	Maximum gap at window opening perimeter: 1/4 inch.

2.	Maximum offset from level: 1/8 inch.

3.2	ADJUSTING

A.	Adjust blinds for smooth operation and to clear window operating hardware.

3.3	DEMONSTRATION

A.	Demonstrate proper operation and maintenance of blinds to Owner.

3.4	SCHEDULE

A.	Shade Type 1:

1.	Description: Motorized interior solar control shade.

2.	Color: White.

B.	Shade Type 2:

1.	Description: Motorized interior room darkening shade with blackout fabric.

2.	Color: Black.

C.	Shade Type 3:

1.	Description: Motorized interior dual solar and room darkening shade with blackout fabric.

2.	Color: White/white.

END OF SECTION